1. Start Up the TX2 in Forced Reset Mode
2. Plug in to a Ubuntu Linux 16 or 18 Host Computer
  1. Remember the host will probably not be ARM proc, but the TX2 is ARM aarch64 for purposes of building software packages
3. Installed Nvidia JetPack SDK on the host computer – small Lenovo w/Ubuntu 18
  1. Needs a network connection
  2. Check for all updates on the Host, then check again
4. Connect TX2 to host via supplied USB cable
5. Run the JetPack Installer on the Host to install on the TX2
  1. Will take significant time to install JetPack on Host, download the Software and Flash the TX2 for the first time.
  2. JetPack caches the downloads locally on the host for next time
  3. The JetPack installation process will pause part way through
  4. Requires the TX2 to complete its Initial Setup on the TX2
  5. Complete setup on the TX2 only through the initial setup steps (including a static IP if you have one – but static is not required at this point)
6. Return to the Host Computer and complete the installation of JetPack software.
  1. You can use the default IP address to complete the setup, but you will want to make sure you note the Username and Password of the TX2
  2. Complete install will require a few hours and can run unattended, however it will require you to click Finish and Exit to complete the install. If you click skip or go back at any point it will need to repeat the previous steps (potentially hours).
  3. If the TX2 does not have an internet connection you will get “Connection Failed” errors, these can be ignored for the time being.
7. Download, Build and Install the jetson-inference project from Git
  1. https://github.com/dusty-nv/jetson-inference.git
  2. Follow the instructions in the Hello World tutorial to setup and test AI – cmake will be required many times – make sure these steps complete without errors
    1. $ sudo apt-get update
    2. $ sudo apt-get install git cmake libpython3-dev python3-numpy
    3. $ git clone --recursive https://github.com/dusty-nv/jetson-inference
    4. $ cd jetson-inference
    5. $ mkdir build
    6. $ cd build
    7. $ cmake ../
    8. $ make
    9. $ sudo make install
    10. $ sudo ldconfig
8. The Python functionality of this project is implemented through Python extension modules that provide bindings to the native C++ code using the Python C API. While configuring the project, the repo searches for versions of Python that have development packages installed on the system, and will then build the bindings for each version of Python that's present (e.g. Python 2.7, 3.6, and 3.7). It will also build numpy bindings for versions of numpy that are installed.
  1. By default, Ubuntu comes with the libpython-dev and python-numpy packages pre-installed (which are for Python 2.7). Although the Python 3.6 interpreter is pre-installed by Ubuntu, the Python 3.6 development packages (libpython3-dev) and python3-numpy are not. These development packages are required for the bindings to build using the Python C API.
  2. So if you want the project to create bindings for Python 3.6, install these packages before proceeding:
  3. $ sudo apt-get install libpython3-dev python3-numpy
9. Installing these additional packages will enable the repo to build the extension bindings for Python 3.6, in addition to Python 2.7 (which is already pre-installed). Then after the build process, the jetson.inference and jetson.utils packages will be available to use within your Python environments.
  1. Install the selected Models
    1. Note the amount of space required – TX2 has 8GB available – installing all the models will take a little over 2GB
  2. Compile the Models
    1. $ cd jetson-inference/build # omit if working directory is already build/ from above
    2. $ make
    3. $ sudo make install
    4. $ sudo ldconfig
  3. In the build tree, you can find the binaries residing in build/aarch64/bin/, headers in build/aarch64/include/, and libraries in build/aarch64/lib/. These also get installed under /usr/local/ during the sudo make install step.
  4. The Python bindings for the jetson.inference and jetson.utils modules also get installed during the sudo make install step under /usr/lib/python*/dist-packages/. If you update the code, remember to run it again.
10. You will need to be in the correct directory to run the examples
  1. cd jetson-inference/build/aarch64/bin
  2. Run the Imagenet Object ID test
    1. ./imagenet-console.py --network=googlenet images/orange_0.jpg output_0.jpg # --network flag is optional
11. Install VS Code – OSS version for ARM processors
  1. Install CURL
    1. sudo apt-get install curl
  2. curl -s https://packagecloud.io/install/repositories/swift-arm/vscode/script.deb.sh | sudo bash
  3. sudo apt-get install code-oss
  4. Code OSS will be installed in /usr/share/applications/
  5. Once installed you can pin it to the dock
  6. Install the Python Extension in VS Code
  7. Install pylint
    1. sudo pip3 install pylint
  8. Enjoy!
12. Set up LIDAR
  1. plug in to USB
  2. install the rplidar libraries
    1. sudo pip3 install rplidar
  3. Python test code from RPLIDAR
    1. from rplidar import RPLidar
lidar = RPLidar('/dev/ttyUSB0')

info = lidar.get_info()
print(info)

health = lidar.get_health()
print(health)

for i, scan in enumerate(lidar.iter_scans()):
print('%d: Got %d measurments' % (i, len(scan)))
if i > 10:
break

lidar.stop()
lidar.stop_motor()
lidar.disconnect()
  2. If you get the following error when you try to connect: rplidar.RPLidarException: Failed to connect to the sensor due to: [Errno 13] could not open port /dev/ttyUSB0: [Errno 13] Permission denied: '/dev/ttyUSB0'
    1. you need to add yourself to the tty or dialout Group then restart
      1. sudo gpasswd -a autobot tty
      2. sudo usermod -a -G dialout autobot
      3. Restart
  3. Install and test rplidar SDK
    1. clone the repository
      1. git clone https://github.com/Slamtec/rplidar_sdk.git
      2. cd rplidar_sdk/sdk
      3. make
      4. cd output/Linux/Release
      5. ./simple_grabber /dev/ttyUSB0
  4. Install and test ROS (Melodic)
    1. cd to Home directory
      1. cd ~
    2. Configure your Ubuntu repositories to allow "restricted," "universe," and "multiverse." You can follow the Ubuntu guide for instructions on doing this.
      1. https://help.ubuntu.com/community/Repositories/Ubuntu
    3. Setup your computer to accept software from packages.ros.org.
      1. sudo sh -c 'echo "deb http://packages.ros.org/ros/ubuntu $(lsb_release -sc) main" > /etc/apt/sources.list.d/ros-latest.list'
    4. Set up your keys
      1. curl -sSL 'http://keyserver.ubuntu.com/pks/lookup?op=get&search=0xC1CF6E31E6BADE8868B172B4F42ED6FBAB17C654' | sudo apt-key add -
    5. Update package list
      1. sudo apt update
    6. install ROS Desktop (Not Desktop-Full)
      1. sudo apt install ros-melodic-desktop
    7. Initialize ROS Dep
      1. sudo rosdep init
      2. rosdep update
    8. Environment Setup - It's convenient if the ROS environment variables are automatically added to your bash session every time a new shell is launched:
      1. echo "source /opt/ros/melodic/setup.bash" >> ~/.bashrc
      2. source ~/.bashrc
    9. Dependencies for building packages
      1. sudo apt install python-rosinstall python-rosinstall-generator python-wstool build-essential
    10. Check your installation
      1. printenv | grep ROS
    11. Source the Environment
      1. source /opt/ros/melodic/setup.bash
    12. install catkin_pkg
      1. sudo pip3 install catkin_pkg
  5. Create a catkin workspace
    1. mkdir -p ~/bot_catkin_ws/src
    2. cd bot_catkin_ws
    3. you may need to install cmake
      1. download the tar ball
      2. extract
      3. ./bootstrap && make && sudo make install
    4. The first time in any new directory you must use the following, after that you can use just cmake
      1. catkin_make -DPYTHON_EXECUTABLE=/usr/bin/python3 -DPYTHON_INCLUDE_DIR=/usr/include/python3.6m -DPYTHON_LIBRARY=/usr/lib/libpython3.6m.so
    5. Source the new catkin overlay
      1. source devel/setup.bash
    6. To make sure your workspace is properly overlayed by the setup script, make sure ROS_PACKAGE_PATH environment variable includes the directory you're in.
      1. echo $ROS_PACKAGE_PATH
    7. cd /src
    8. clone the rplidar_ros
      1. git clone https://github.com/Slamtec/rplidar_ros.git
    9. cd ..
    10. Confirm the overlay
      1. source devel/setup.bash
    11. Run catkin_make
      1. catkin_make
    12. roslaunch rplidar_ros view_rplidar.launch
    13. Might need to change the USB port in the launch file
      1. ProTip for sorting USB:
        1. Store list of devices before plugging in Device
          1. ls /dev/ > dev_list_1.txt
        2. Then run this after you plug it in
          1. ls /dev/ | diff --suppress-common-lines -y – dev_list_1.txt

## RPLIDAR Won’t stop
1. Power problem
2. it looks power problem about my rplidar.
3. i used 5V/1A power connect. but when i see CPU monitor, i think it was lack about using RPlidar
4. so i connect power-supplied USB 3.0 hub with RPlidar.
5. add 2 lines of command
6. when i use rplidar i always insert 2 lines of command $ source /home/{user}/catkin_ws/devel/setup.bash $ source /opt/ros/kinetic/setup.bash
with 2 solutions, i can start , stop my rplidar.

## PCA9685 Adafruit PCM
https://github.com/jetsonhacks/JHPWMDriver
https://www.jetsonhacks.com/2016/01/11/imu-and-pwm-driver-over-i2c-for-nvidia-jetson-tx1/

https://github.com/adafruit/Adafruit_CircuitPython_ServoKit
sudo pip3 install adafruit-circuitpython-servokit

## Using ROS

1. If you are ever having problems finding or using your ROS packages make sure that you have your environment properly setup. A good way to check is to ensure that environment variables like ROS_ROOT and ROS_PACKAGE_PATH are set:
  1. printenv | grep ROS
2. Need to run this in every new shell unless added to .bashrc
  1. source /opt/ros/melodic/setup.bash
3. To make sure your workspace is properly overlayed by the setup script, make sure ROS_PACKAGE_PATH environment variable includes the directory you're in.
  1. echo $ROS_PACKAGE_PATH
4. Make sure to allow access to the USB
  1. sudo chmod 666 /dev/ttyUSB0

Notes:

  WARNING: The script jupyter-console is installed in '/home/autobot/.local/bin' which is not on PATH.
  Consider adding this directory to PATH or, if you prefer to suppress this warning, use –no-warn-script-location.

### System-wide environment variables
A suitable file for environment variable settings that affect the system as a whole (rather than just a particular user) is /etc/environment. An alternative is to create a file for the purpose in the /etc/profile.d directory.
### /etc/environment
This file is specifically meant for system-wide environment variable settings. It is not a script file, but rather consists of assignment expressions, one per line.
FOO=bar
Note: Variable expansion does not work in /etc/environment.
### /etc/profile.d/*.sh
Files with the .sh extension in the /etc/profile.d directory get executed whenever a bash login shell is entered (e.g. when logging in from the console or over ssh), as well as by the DisplayManager when the desktop session loads.
You can for instance create the file /etc/profile.d/myenvvars.sh and set variables like this:
export JAVA_HOME=/usr/lib/jvm/jdk1.7.0
export PATH=$PATH:$JAVA_HOME/bin
## Setting USB Environment Variables 1. find out what's on ttyUSB:
dmesg | grep ttyUSB

2. list all attributes of the device:
udevadm info --name=/dev/ttyUSBx –attribute-walk

(with your device number(s) instead of x, of course). Pick out a unique identifier set, eg idVendor + idProduct. You may also need SerialNumber if you have more than one device with the same idVendor and idProduct. SerialNumbers ought to be unique for each device.

ID_VENDOR=Silicon_Labs
ID_VENDOR_ID=10c4
ID_MODEL_ID=ea60

3. Create a file /etc/udev/rules.d/99-usb-serial.rules with something like this line in it:

SUBSYSTEM=="tty", ATTRS{idVendor}=="1234", ATTRS{idProduct}=="5678", SYMLINK+="your_device_name"

(assuming you don't need a serial number there, and of course with the numbers for idVendor and idProduct that you found in step 2.

4. Load the new rule:
sudo udevadm trigger

5. Verify what happened:

ls -l /dev/your_device_name
will show what ttyUSB number the symlink went to. If it's /dev/ttyUSB1, then verify who owns that and to which group it belongs:
ls -l /dev/ttyUSB1

Then just for the fun of it:
udevadm test -a -p $(udevadm info -q path -n /dev/your_device_name)

symlink for our bot : uart_bridge

### Flip the Camera Image:
1. set flipMethod to 0 in the file utils/camera/gstCamera.cpp: line 416
#if NV_TENSORRT_MAJOR > 1 && NV_TENSORRT_MAJOR < 5 // if JetPack 3.1-3.3 (different flip-method)
        const int flipMethod = 0; // Xavier (w/TRT5) camera is mounted inverted
        #else
        const int flipMethod = 0;
        #endif

2. go to:
cd jetson-inference/build
make clean
cmake ../
make
sudo make install

### LIDAR Demo

cd ~/rplidar
source devel/setup.bash
roslaunch rplidar_ros view_rplidar.launch